## Slide 1: Systems research in the AI era
Dushyanth Narayanan
Microsoft Research Future AI Infrastructure (MSR FAI)

## Slide 2: It’s a great time to be a systems researcher
AI is the most important workload
Bigger models  new capabilities
Progress relies on scale
Scale is what we do
Publication year
Training compute (FLOPs)
Training compute of frontier AI models grows by 4-5x per year | Epoch AI

## Slide 3: MSR Future AI Infrastructure (FAI)
Systems innovation
Memory
Storage
Network
Compute
ML models
Systems
Hardware
MSR FAI spans MSR labs and disciplines
Partnering with Microsoft product groups and external partners
Efficiency
Time
Network Compute Memory Storage
We need research across the stack
And across disciplines
We are hitting hardware scaling limits
Hardware/software codesign

## Slide 4: The scale of AI infrastructure is staggering
Inside the world’s most powerful AI datacenter - The Official Microsoft Blog

## Slide 5: Silicon scaling is hitting limits
AMD MI300X
2024
NVIDIA GB200
2025
Cerebras W3
high manufacturing costs
poor hardware yield
large failure domain
power & heat challenges
NVIDIA H100 2022

## Slide 6: Power and package size are big challenges
Blackwell GPU
2x full reticle compute dies
8x HBM modules
33 mm
26 mm

## Slide 7: What is different about AI workloads?
Hardware ultra-specialization
New systems challenges and opportunities
Predictable, regular data access
Extreme memory bandwidth requirements
Embarrassingly parallel compute
Very high network bandwidth requirements

## Slide 8: Today’s talk
Scaling clusters without melting the racks
Rethinking memory architectures for AI
Program transformation for specialized hardware

## Slide 9: Cluster scaling is hitting power limits
Rack power density keeps growing
Power, cooling, etc.
Blackwell NVL72
GPUs

## Slide 10: Bandwidth-reach tradeoff
~10x oversubscription
NVLink 7.2 Tbps/GPU 72 GPUs
GPU
NVIDIA Blackwell NVL72
Ethernet/IB 800 Gbps/GPU
100,000s GPUs
Optics (lasers)
High power, failure-prone, long reach
Copper
Low power, reliable, short reach
Can we break this trade-off?

## Slide 11: Wide-and-slow to the rescue
…
Few channels operating at high speed (e.g., 800 Gbps = 8 x 100 Gbps)
Many channels operating at low speed (e.g., 800 Gbps = 400 x 2 Gbps)
Commodity technologies
Low power
High reliability
Mosaic: Breaking the Optics versus Copper Trade-off with a Wide-and-Slow Architecture and MicroLEDS

## Slide 12: Switches still consume power
Circuit switching: an old idea whose time has come?
GPU 1
GPU 4
Packet switch
GPU 2
GPU 3
GPU 1
GPU 4
GPU 2
GPU 3
Property | Packet switch Broadcom Tomahawk 5 | Circuit switch Calient S320
Power | 500 W | 45 W
Transceiver power | 900 W | 0 W
Cut through latency | ~600 ns | ~ 0 ns
Port count | 512 | 320
Reconfiguration time | N/A | 100 ms
Challenge: flexibility!
Circuit switch

## Slide 13: Today’s talk
Scaling clusters without melting the racks
Rethinking memory architectures for AI
Automatic quantization for specialized hardware

## Slide 14: Compute-memory gap is widening
10x
HBM based GPUs
Widened by 10x in 12 years
Despite HBM improvements

## Slide 15: HBM: can’t live with it, can’t live without it
Complex manufacturing and packaging
Unreliable
Adds significant cost and power
Still not enough bandwidth!
Plotting The Next Semiconductor Road Map
High Bandwidth Memory (HBM) is the only option today to achieve good bandwidth to AI data

## Slide 16: Many operations are memory bound
This is getting worse
  Long contexts
  Agentic workloads
  Multimodal models
Prefill Training
Compute utilization < 0.5%

## Slide 17: Specialization for compute is happening
NVIDIA Rubin CPX
NVIDIA Rubin CPX Accelerates Inference Performance and Efficiency for 1M+ Token Context Workloads | NVIDIA Technical Blog
No HBM
4x FP4 FLOPS of B200
0.5x memory bandwidth
Workloads will become more memory-bound overall
  Amdahl’s Law
We also need to specialize for bandwidth
Another Giant Leap: The Rubin CPX Specialized Accelerator & Rack

## Slide 18: The challenge is data movement not access
Data movement dominates energy
Energy limits bandwidth
Architecting an Energy-Efficient DRAM System for GPUs Chatterjee et al, ISCA 2017
HBM3e (our model)

## Slide 19: Re-emergence of PIM (Program in Memory)
Compute on DRAM die
   Very close to memory
   DRAM die is poor fit for compute
Aquabolt-XL: Samsung HBM2-PIM with in-memory processing for ML accelerators and beyond (Hotchips 2021)
[2504.16112] HPU: High-Bandwidth Processing Unit for Scalable, Cost-effective LLM Inference via GPU Co-processing
Wimpy compute die
   Unchanged HBM + packaging
   Unchanged HBM + packaging
Compute on base die
  HBM3 does not support logic layer
  HBM4 will support it!
Hybrid memory cube (HMC) (HotChips 2011)

## Slide 20: Example: PIM for decode attention
What does the interconnect look like?
Can we use circuit switching?
Latency and packet drops
Fault tolerance
Can we automate the partitioning?
Are there other use cases?
Collective
Collective
Compute optimized
Bandwidth optimized

## Slide 21: The future is heterogenous and disaggregated
Specialized hardware
Scalable networking
Packet
switch
Compute optimized
Bandwidth optimized
Circuit switch
Compute optimized
Bandwidth optimized
Circuit switch
Ultra high bandwidth optics
New memory technologies
New compute
architectures
3D stacked optics
Analog/optical computing

## Slide 22: Today’s talk
Scaling clusters without melting the racks
Rethinking memory architectures for AI
Program transformation for specialized hardware

## Slide 23: Multiple ways to improve AI efficiency
Lower $
Lower W
Higher Velocity

## Slide 24: Quantizing models for NPU
GPU
96 GB HBM
fp16
NPU
16 GB LPDDR
int4

## Slide 25: Quantization workflow
QuaRot: SOTA quantization technique
New model released for GPU
Quantized model for NPU
Insert new ops into source code
Compute rotation tensors using calibration dataset
Validate perf and accuracy
Complex and time consuming!

## Slide 26: Model rotation as program synthesis problem
Many equivalent operator graphs
  (Un)rotation
  Operator fusion
  Reordering
With constraints
  Matmul inputs are quantized
  Quantization op inputs are rotated
  …
Minimize graph execution cost
Op
Rotate
Quantize
W
Q
X
Op
Quantize
W @ Q
X

## Slide 27: Aqua compiler
PyTorch
Module
Aten
graph
Constraints
data flow
rotation
fusion
cost
Tensor schedule
rotation
quantization
unrotation
Graph
rewriter
Quant’d
module
Frontend
Solver
Backend
satisfies:
peak memory below limit
latency is minimal

## Slide 28: New opportunities for PL techniques
Traditional program analysis
  Loops
  Data structures
  Aliasing
  Concurrency
AI program analysis
  Tensor computation / linear algebra
  Data parallel hardware
  Collectives
  Global optimization

## Slide 29: We’ve just started exploring
Mosaic: Breaking the Optics versus Copper Trade-off with a Wide-and-Slow Architecture and MicroLEDS (SIGCOMM 2025 best paper)
Storage Class Memory is Dead, All Hail Managed-Retention Memory: Rethinking Memory for the AI Era (HotOS ‘25)
Good things come in small packages: Should we build AI clusters with Lite-GPUs? (HotOS ‘ 25)
Towards Memory Specialization: A Case for Long-Term and Short-Term RAM (DIMES ‘25)
Analog optical computer for AI inference and combinatorial optimization | Nature

## Slide 30: Efficiency and scalability are crucial for AI
Systems innovation
Memory
Storage
Network
Compute
ML models
Systems
Hardware
Efficiency
Time
Network Compute Memory Storage
We need research across the stack
And across disciplines
We are hitting hardware scaling limits
Hardware/software codesign